## Slide 1
A Post-processing Approach for Solar Power Combined Forecasts of Ramp Events
Mohamed Abuella
Supervised by:
Prof. Badrul Chowdhury
A dissertation submitted to the faculty of
The University of North Carolina at Charlotte
in partial fulfillment of the requirements
for the degree of Doctor of Philosophy in
Electrical Engineering
Charlotte
October 1st, 2018

## Slide 2
Dissertation Organization
Dissertation Layout
Presentation Outline
Modeling and Results
Highlights, Motivation, Literature Review, Problem Statement & Contribution,
Theoretical Background & Methodology
Conclusions and Future Work
https://www.researchgate.net/publication/328757565_A_Post-processing_Approach_for_Solar_Power_Combined_Forecasts_of_Ramp_Events/download

## Slide 3
A post-processing approach combines and improves solar power forecasts.
The approach also adjusts the combined forecasts in terms of ramp events.
A classification of all possible thresholds and classes of ramp event forecasts.
A customized cost function for imbalanced classification of ramp events.
Suitable metrics for the feature selection process and performance evaluation.
An uncertainty analysis for probabilistic forecasts of solar power ramp events.
Highlights

## Slide 4
https://www.seia.org/us-solar-market-insight (June 12, 2018, insight of US Solar Market)
Motivation
Source: SEIA/GTM Research
A U.S. PV solar market study * prepared by Solar Energy Industries Association (SEIA)
and GTM Research

## Slide 5
Illustration of the motivation of PV solar power forecasts
PV Solar Power Generations
are Too Variable
Reducing
Cost
and Pollution
PSupply = PDemand +PLoss
Coordination with Operating Reserves and Energy Storage
Systems
Why Forecast?
Motivation

## Slide 6
Hong, Tao, et al. "Probabilistic energy forecasting: Global energy forecasting competition 2014 and beyond." International Journal of Forecasting 32.3 (2016): 896-913.
Maturity quadrant of the energy forecasting subdomains (SPF: solar power forecasting; LTLF: long term load forecasting; EPF: electricity price forecasting; WPF: wind power forecasting; STLF: short term load forecasting) .
Challenges
Motivation

## Slide 7
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
0.18
0.2
0.22
Days
R
M
S
E
The RMSE of the Models
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
M11
M12
M13
M14
M15
M16
M17
M18
M19
M20
M21
M22
M23
M24
Combined Forecasts
Average Forecasts
-Probabilistic Forecasts;
-Ramp Event Forecasts;
-Electricity System Operation Adjustments for
Optimal Implementation of the Forecast.
-Better Evaluation Methods for Forecasts;
-Accurate V.G. Forecasting;
-Forecasts for PV Solar Distributed Generation
Systems “Behind-the-Meter Resources”;
-Ensemble Forecasts;
Solar Forecasting: Methods, Challenges, and Performance (IEEE Power & Energy Magazine Nov. 2015)
By Aidan Tuohy, John Zack, Sue Ellen Haupt, Justin Sharp, Mark Ahlstrom, Skip Dise, Eric Grimit, Corinna Möhrlen, Matthias Lange, Mayte Garcia Casado, Jon Black,Melinda Marquis, and Craig Collier.
-Study the economic value of V.G. forecasting;
These are the objectives of the ongoing research on this field that are addressed and recommended for the academy and industry.
7
Challenges
Motivation

## Slide 8
# M. Sengupta, A. Habte, C. Gueymard, S. Wilbert, and D. Renne, Best practices handbook for the collection and use of solar resource data for solar energy applications," Tech. rep., National Renewable Energy Lab.(NREL), Golden, CO (United States), 2017
Literature Review
Yang, D., Kleissl, J., Gueymard, C. A., Pedro, H. T., & Coimbra, C. F. (2018). History and trends in solar irradiance and PV power forecasting: A preliminary assessment and review using text mining. Solar Energy. (**This review paper published in 2018, and reviewing 1000 solar forecast studies).
Taxonomy of solar forecasting methods based on temporal and spatial resolution#
CM-sat: cloud motion by satellite images;
CM-SI: cloud motion by sky-imagers
NWP: Numerical weather prediction Systems
Statistical models: blending and post-processing all of the methodologies.

## Slide 9
[R.1] Schmidt, T., Calais, M., Roy, E., Burton, A., Heinemann, D., Kilper, T., & Carter, C. (2017). Short-term solar forecasting based on sky images to enable higher PV generation in remote electricity networks. Renewable Energy and Environmental Sustainability.
[R.2] Palmer, D., Koubli, E., Cole, I., Betts, T., & Gottschalg, R. (2018). Satellite or ground-based measurements for production of site specific hourly irradiance data: Which is most accurate and where?. Solar Energy, 165, 240-255.
[R.3] Bessa, R. J., Trindade, A., & Miranda, V. (2015). Spatial-temporal solar power forecasting for smart grids. IEEE Transactions on Industrial Informatics, 11(1), 232-241.
[R.4] Cui, M., Zhang, J., Florita, A., Hodge, B. M., Ke, D., & Sun, Y. (2015, August). Solar power ramp events detection using an optimized swinging door algorithm. In ASME 2015 International Design Engineering and Computers and Information in Engineering Conference.
Main methods for solar irradiance / power ramp events:
Forecast Approaches:
a) Physical models to track the cloud motion: sky imagers and satellite systems.
b) Statistical models that are selected based on forecasts of weather conditions.
2) Identification/Detection Approaches:
a) Anomaly detection methods, such as swinging door algorithm [R.4].
b) Classification by using machine learning techniques.
Shadow projection by sky imagine devices [R.1]
Raw and projected cloud map form sky imaging devices [R.1]
Literature Review

## Slide 10
Problem Statement and Contribution
Kleissl, J. (2013). Solar energy forecasting and resource assessment. Academic Press.
Inman, R. H., Pedro, H. T., & Coimbra, C. F. (2013). Solar forecasting methods for renewable energy integration. Progress in energy and combustion science, 39(6), 535-576.
Combining of different forecasts can reduce the systemic bias of the individual models, boost the overall accuracy, and make the performance more robust, but it also smooths out the sharp changes of the forecasts, which leads to reduced accuracy of the combined forecasts for ramp events.
The Problem Statement
The post-processing methods (MOS) are affecting the ramp event forecasts by smoothing the sharp changes in the raw forecasts. (Kleissl 2013; Inman et al. 2013)

## Slide 11
Problem Statement and Contribution
Due to the issue that was highlighted (Kleissl 2013; Inman et al. 2013), it is therefore, there is room for improvement by applying the proposed approach for adjusting the combined forecasts of solar power in terms of ramp events.
To the best of our knowledge, this is the first attempt to tackle this issue of the combined forecasts for solar power ramp events.
The Contribution
A post-processing approach combines and improves solar power forecasts.
The approach also adjusts the combined forecasts in terms of ramp events.
A classification of all possible thresholds and classes of ramp event forecasts.
A customized cost function for imbalanced classification of ramp events.
Suitable metrics for the feature selection process and performance evaluation.
An uncertainty analysis for probabilistic forecasts of solar power ramp events.

## Slide 12
Flowchart of Solar Power Forecasts
Graphical Abstract of the Proposed Adjusting Approach

## Slide 13
Block diagram of the adjusting approach
Random
Forest
fit by
MSE
F
&
MSE
RR
Day
-
ahead Forecasts
including the past forecasts
Outcomes
:
MLR
,
ANN
,
SVR
Hour
-
ahead Forecasts
including the past forecasts
Outcomes
:
Persistence and
Combined Forecasts
Ramp Rates of
Day
-
ahead
Forecasts
Adjusted Hour
-
ahead Forecasts
Ramp Rates of
Hour
-
ahead
Forecasts
Combining by
Random Forest
Statistical
&
AI Models
Weather Data
(
NWP
)
PV System
Data
Persistence
Model
Forecasting Stage
Combining Stage
Adjusting Stage
Graphical Abstract of the Proposed Adjusting Approach

## Slide 14
Block diagram of the adjusting approach
Flowchart of Solar Power Forecasts
Pre
-
Processing
·
Outlier detection and
data cleansing
·
Feature engineering
Weather Data
·
Solar irradiance
·
Temperature
·
Cloud coverage
·
Humidity
·
...
etc
.
PV System Data
·
Measured PV power output
·
Location and modules type
,
orientation
,
tilt
,
..
etc
.
Forecasting Models
·
Persistence model
·
Statistical models
·
Artificial intelligence models
Point forecast
Post
-
Processing
·
Ensemble
·
Analog ensemble
Probabilistic forecast
Combining the models’ outcomes
by ensemble learning
Random
Forest
fit by
MSE
F
&
MSE
RR
Day
-
ahead Forecasts
including the past forecasts
Outcomes
:
MLR
,
ANN
,
SVR
Hour
-
ahead Forecasts
including the past forecasts
Outcomes
:
Persistence and
Combined Forecasts
Ramp Rates of
Day
-
ahead
Forecasts
Adjusted Hour
-
ahead Forecasts
Ramp Rates of
Hour
-
ahead
Forecasts
Combining by
Random Forest
Statistical
&
AI Models
Weather Data
(
NWP
)
PV System
Data
Persistence
Model
Forecasting Stage
Combining Stage
Adjusting Stage
Graphical Abstract of the Proposed Adjusting Approach

## Slide 15
Ramp Events During a Cloudy Day
Some ramps are with low rates, while others with high rates.
Ramp rate, =
Ramp rate, =
For the illustrated cloudy day below:
where P(t) is the solar power of the target hour, it can also be its forecast F(t); D is the time duration for which the ramp rate is determined.
Solar Power Ramp Rates
Solar power ramp rate (RR) is the change of solar power during a certain time interval.

## Slide 16
There are several applications of power systems that rely on solar power ramp event forecasts
Potential Applications
Optimizing the voltage regulation equipment.
Control schemes of energy storage systems.
EPEX: European power exchange spot trading
Optimizing the Transformer's Tap Changer position sequences using the solar forecast
Trading & dispatching the operating reserve.
Managing the ramp capability / system flexibility with high-level of renewable energy integration.
Distribution level:
Transmission / bulk level:

## Slide 17
Data Preprocessing
Data Description:
B. Marion, A. Anderberg, C. Deline, J. del Cueto, M. Muller, G. Perrin, J. Rodriguez, S. Rummel, T. J. Silverman, F. Vignola, et al., New data set forvalidating pv module performance models," in Photovoltaic Specialist Conference (PVSC), 2014 IEEE 40th, pp. 1362{1366, IEEE, 2014.
https://crowdanalytix.com/contests/global-energy-forecasting-competition-2014-probabilistic-solar-power-forecasting
Dataset | Golden, CO | Cocoa, FL | Eugene, OR | Canberra
Country | USA | USA | USA | Australia
Climate type | Semi-arid | Subtropical | Marine coast | Oceanic
Latitude (°, -S) | 39.74 | 28.39 | 44.05 | -35.16
Longitude (°, -W) | -105.18 | -80.46 | -123.07 | 149.06
Elevation above sea (m) | 1798 | 12 | 145 | 595
Number of panels | 11 | 11 | 11 | 8
Panel tilt (°) from horizontal | 40 | 28.5 | 44 | 36
Panel orientation (°) clockwise from North | 180 | 180 | 180 | 38
Total capacity (W) | 1252 | 1272 | 1290 | 1560
Time period of observations | Aug. 2012 to Sep. 2013 | Jan. 2011 to March 2012 | Dec. 2012 to Jan. 2014 | April 2012 to May 2014
Data resolution | 15min | 5min | 5min | 1hr
Missing (% of observations) | 18% | 17% | 10% | 0%
Variability (data resolution) Std.Div. | (15min) 0.256 (1hr) 0.119 | (5min) 0.251 (1hr) 0.164 | (5min) 0.250 (1hr) 0.161 | (1hr) 0.259

## Slide 18
PV solar system is near Canberra, Australia, consisting of 8 panels, its nominal power of (1560W), and panel orientation 38° clockwise from the north, with panel tilt (of 36°). The historical observed solar power data are normalized to the rated capacity (i.e., 1560W).
https://crowdanalytix.com/contests/global-energy-forecasting-competition-2014-probabilistic-solar-power-forecasting
Weather predictions are produced by a global numerical weather prediction system, European Centre for Medium-Range Weather Forecasts (ECMWF).
Data Preprocessing
Data partition into training and testing sets
Available data
No. | Input Variable, (X)
10 | Surface thermal radiation down
11 | Top net solar radiation
12 | Total precipitation
13 | Heat Index
14 | Wind Speed
15 | Hours
16 | Months
17 | Days of Month
18 | Days of Year
 | Month | Year | Partition
From | April | 2012 | Training Set
To | May | 2013 | 
From | June | 2013 | Testing Set
To | May | 2014 | 
No. | Input Variable, (X)
1 | Cloud Water Content
2 | Cloud Ice Content
3 | Surface Pressure
4 | Relative Humidity
5 | Cloud Cover
6 | 10m - U Wind
7 | 10m - V Wind
8 | 2-m Temperature
9 | Surface solar radiation down
Data Description:

## Slide 19
Data Preprocessing
Scatter plot of the observed solar power vs. Solar Irradiance
Solar Power vs. Surface Solar Irradiance Down (SSRD) provide by NWP
Benchmark Data
Data Cleansing
Select most Effective Variables
Scatter & Box plots the Data
Greedy Search - Wrapping Approach
=
Flowchart of Data Preparation

## Slide 20
Data Preprocessing
Benchmark Data
Data Cleansing
Select most Effective Variables
Scatter & Box plots the Data
Greedy Search - Wrapping Approach
Flowchart of Data Preparation
September 24th, 2013
One week:
August 14th to 20th ,2012
Filling of missing data
by interpolation
There are missing data:
All minutes at hour=9 and some minutes at hour=10, 12, and 14.

## Slide 21
Flowchart of Data Preparation
Data Preprocessing
Pick up a feature from the available features set;
Run the model with this feature;
Score the model, by using the following score: Max(Diff. Index),
where Diff. Index is the difference between true and false ramp events;
Add another feature to the selected features;
Repeat steps 2 and 3;
Choose subset of features with the best score, remove the selected from the available features;
Repeat steps 1 to 6;
If there is no longer any feature to select, Stop.
Objective: Increase the true events, Decrease the false events.
& F
Benchmark Data
Data Cleansing
Select most Effective Variables
Scatter & Box plots the Data
Greedy Search - Wrapping Approach

## Slide 22
Data Preprocessing
Models' parameters and their selected input variables

## Slide 23
Evaluation Metrics
These are negatively oriented metrics except the skill score,
which is the higher is the better.
Pbq,i (Fq, ) =
Quantiles, q[1- 99]

## Slide 24
Confusion matrix of possible cases of solar power ramp events
The evaluation metrics to assess the classification for solar ramp events:
The most suitable metrics for our application are the Diff. Index and the F1 score.
Objective: Increase the true events, Decrease the false events.
& F
Evaluation Metrics

## Slide 25
Regression or Classification Models
Block diagram of PV solar power ramp event forecasting models
Methodology
Task:
(Regression /
Classification)
Input Variables:
(Solar power and weather forecasts)
Output Variable:
(PV solar power ramp event forecasts)
Training Dataset:
(Past solar power and weather data)
Fitting / Learning Algorithm of the
Forecasting Model

## Slide 26
Model N
Weather Data
Ensemble Learning (RF) for Combining of Forecasts
Combined Forecasts
Individual Forecasts of PV Solar Power Ramp Events
Model A
Model B
Fcomb=WA*MA+ WB*MB + WC*MC ….+ WN*MN
:
Methodology
Method of Combining The Models
Random forest (RF) is chosen to be the ensemble learning method for combining the various models’ outcomes.
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.
Ensemble Forecasts: Combining Various Models
General diagram of combining different models

## Slide 27
Probabilistic model
Solar power point forecasts
NWP point forecasts
Probabilistic forecasts of solar power
(a)
(b)
(c)
Methodology
Ensemble-based probabilistic forecasts
Probabilistic Forecasts
Diagram of ensemble-based probabilistic forecasts,
Splitting mechanism of trees in random forest,
Sample of ensemble-based probabilistic forecasts of solar power of 3 days

## Slide 28
Delle Monache, L., Eckel, F. A., Rife, D. L., Nagarajan, B., & Searight, K. (2013). Probabilistic weather prediction with an analog ensemble. Monthly Weather Review, 141(10), 3498-3516.
Alessandrini, S., Delle Monache, L., Sperati, S., & Cervone, G. (2015). An analog ensemble for short-term probabilistic solar power forecast. Applied energy, 157, 95-110.
Analog Ensemble (AnEn) method:
where denotes the given point forecast at an hour Hr, for which the prediction interval will be estimated, the point forecasts at the same hour of the day.
Schematic diagram of analog ensemble method
= 0.1
Probabilistic Forecasts
Methodology

## Slide 29
Methodology
Schematic diagram of persistence probabilistic method
Persistence probabilistic method:
Probabilistic Forecasts
The 10, 20 and 30 recent observed powers are carried out.
It is found that the recent 10 observed solar powers at the given hour with CDF distribution achieve more accurate persistence probabilistic forecasts.

## Slide 30
Methodology
(a) Solar power observations of the given day, (b) histograms of the random forest outcomes of the forecast at 12:00pm,(c) estimated CDFs for the probabilistic forecasts at 12:00pm
Probabilistic Forecasts
Probability distributions of the random forest outcomes at 12:00 pm on May 29th
(b)
(a)
(c)

## Slide 31
Combining by Ensemble Learning
Producing Different Models’ Outcomes
Adjusting and Correcting the Combined Forecasts By the Ramp Rates
Schematic and block diagrams of the adjusting post-processing approach
Methodology

## Slide 32
Combined forecasts of solar power for a cloudy day before and after applying the adjusting
Improving Combined Forecasts
Modeling and Results
Implementing the adjusting approach for Improving Combined Solar Power Forecasts

## Slide 33
Method | Persistence | MLR | ANN | SVR | Simple Average | Ensemble (Before Adjusting) | Ensemble (After Adjusting)
MBE (Bias)­ | 0.0756 | -0.1498 | -1.852 | -4.291 | -1.554 | 0.0469 | 0.0747
RMSE­ | 0.1209 | 0.0763 | 0.0681 | 0.0700 | 0.0667 | 0.0628 | 0.0523
RMSERR­ | 0.1383 | 0.0771 | 0.0722 | 0.0747 | 0.0796 | 0.0750 | 0.0698
RMSE Improve (%) | 57% | 31% | 23% | 25% | 22% | 17% | ---
Improving Combined Solar Power Forecasts
Chart: RMSE
| June | July | August | September | October | November | December | January | February | March | April | May
Before Adjusting | 0.0626 | 0.0825 | 0.0727 | 0.0705 | 0.0579 | 0.0605 | 0.0507 | 0.0464 | 0.0627 | 0.0755 | 0.0605 | 0.0516
After Adjusting | 0.055 | 0.0646 | 0.0595 | 0.0589 | 0.0502 | 0.0512 | 0.0428 | 0.0397 | 0.0528 | 0.0619 | 0.0481 | 0.0424
Monthly RMSEs of combined forecasts before and after applying the adjusting approach
Comparison of hour-ahead forecasts over a complete year
Improving Combined Forecasts
Modeling and Results

## Slide 34
Graphs of the probabilistic forecasts of the three methods for three days
Probabilistic Forecasts
Improving Combined Forecasts
Modeling and Results
Pbq,i (Fq, ) =
Quantiles, q[1- 99]

## Slide 35
Probabilistic Forecasts
Improving Combined Forecasts
Modeling and Results
Chart: Pinball
| June | July | August | September | October | November | December | January | February | March | April | May
Persistence | 0.0166 | 0.0176 | 0.0182 | 0.0173 | 0.0149 | 0.0191 | 0.0162 | 0.0179 | 0.0215 | 0.0208 | 0.0194 | 0.0137
Before Adjust Analog Ensemble | 0.0099119 | 0.011864 | 0.010507 | 0.011728 | 0.0096928 | 0.010325 | 0.00886 | 0.0079501 | 0.0099336 | 0.012908 | 0.0099013 | 0.0085649
Before Adjust Ensemble | 0.0093377 | 0.012059 | 0.011266 | 0.01145 | 0.0092941 | 0.010424 | 0.0087217 | 0.0075829 | 0.0095473 | 0.013064 | 0.0097881 | 0.0078016
After Adjust Analog Ensemble | 0.0088156 | 0.0090926 | 0.0089271 | 0.010057 | 0.0094771 | 0.0093353 | 0.0078382 | 0.0069557 | 0.0085113 | 0.010115 | 0.0077895 | 0.0072524
After Adjust Ensemble | 0.0087254 | 0.009353 | 0.0095298 | 0.0092475 | 0.0081807 | 0.0087281 | 0.0074299 | 0.0068535 | 0.0079248 | 0.010214 | 0.0078932 | 0.0064907
Month | Pinball |  |  |  |  | Improvement of Adjusted Ensemble Over: |  | 
 | Persistence | Before Adjusting |  | After Adjusting |  |  |  | 
 |  | Analog Ensemble | Ensemble | Analog Ensemble | Ensemble | Persistence | Before adjust AnEn | Before adjust Ensemble
June | 0.0166 | 0.0099 | 0.0093 | 0.0088 | 0.0087 | 47% | 12% | 7%
July | 0.0176 | 0.0119 | 0.0121 | 0.0091 | 0.0094 | 47% | 21% | 22%
August | 0.0182 | 0.0105 | 0.0113 | 0.0089 | 0.0095 | 48% | 9% | 15%
September | 0.0173 | 0.0117 | 0.0114 | 0.0101 | 0.0092 | 47% | 21% | 19%
October | 0.0149 | 0.0097 | 0.0093 | 0.0095 | 0.0082 | 45% | 16% | 12%
November | 0.0191 | 0.0103 | 0.0104 | 0.0093 | 0.0087 | 54% | 15% | 16%
December | 0.0162 | 0.0089 | 0.0087 | 0.0078 | 0.0074 | 54% | 16% | 15%
January | 0.0179 | 0.0080 | 0.0076 | 0.0070 | 0.0069 | 62% | 14% | 10%
February | 0.0215 | 0.0099 | 0.0095 | 0.0085 | 0.0079 | 63% | 20% | 17%
March | 0.0208 | 0.0129 | 0.0131 | 0.0101 | 0.0102 | 51% | 21% | 22%
April | 0.0194 | 0.0099 | 0.0098 | 0.0078 | 0.0079 | 59% | 20% | 19%
May | 0.0137 | 0.0086 | 0.0078 | 0.0073 | 0.0065 | 53% | 24% | 17%
Average | 0.0178 | 0.0102 | 0.0100 | 0.0087 | 0.0084 | 52% | 18% | 16%

## Slide 36
Chart: Improvement of Adjusted Ensemble-based Probabilistic Forecasts Over:
| June | July | August | September | October | November | December | January | February | March | April | May
Persistence | 0.47437 | 0.46858 | 0.47639 | 0.46547 | 0.45096 | 0.54303 | 0.54137 | 0.61712 | 0.6314 | 0.50895 | 0.59313 | 0.52623
Berfore Adjusting Analog Ensemble | 0.11971 | 0.21168 | 0.093023 | 0.21153 | 0.156 | 0.15464 | 0.16141 | 0.13793 | 0.20222 | 0.20871 | 0.20281 | 0.24218
Before Adjusting Ensemble | 0.065571 | 0.22437 | 0.15415 | 0.19234 | 0.11979 | 0.16268 | 0.14811 | 0.096184 | 0.16994 | 0.21819 | 0.19359 | 0.16803
Probabilistic Forecasts
Improving Combined Forecasts
Modeling and Results

## Slide 37
Ramp Classes as following:
Class1: Ramp up of high rate, Tsh
Class2: Ramp up of low rate, |rate| Tsh
Class3: Ramp down of high rate, |rate|Tsh
Class4: Ramp down of low rate, |rate| Tsh
Combined Forecasts of Ramps
Modeling and Results
Objective: Increase the true events, Decrease the false events.
& F
Implementing several classification models to forecasts solar power ramp events
Distribution of the classes of solar power ramp events at threshold (Tsh) =0.4pu/hr.
Classes of solar power ramp events in the case study

## Slide 38
38
kNN
Weather Data
Ensemble Learning (RF) for Combining of Forecasts
Combined Forecasts
Naive Bayes
LDA
DT
Log. Reg
RF
SVM
ANN
Combining classification models for solar power ramp event forecasting
Fcomb=WA*MA+ WB*MB + WC*MC ….+ WN*MN
where WA is an assigned weight for an outcome of model (A)
Implementing several classification models to forecasts solar power ramp events
Combined Forecasts of Ramps
Individual Classification Models for Solar Power Ramp Event Forecasting
Modeling and Results
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.
Objective: Increase the true events, Decrease the false events.
& F

## Slide 39: Available Features for classification of solar power ramp events
 |  | Weather Data |  |  | Day and Hour-ahead Forecasts |  |  |  |  |  | Forward Ramp Rates |  |  | Backward Ramp Rates |  | 
 |  | No. | Variable Name |  | No. |  | Variable Name | RMSE | Horizon |  | No. | Variable Name |  | No. | Variable Name | 
 |  | 1 | Cloud Water Content |  | 15 |  | Persistence Farm 1 | 0.1209 | hour-ahead |  | 31 | MLR |  | 34 | Persistence Farm 1 | 
 |  | 2 | Cloud Ice Content |  | 16 |  | Persistence Farm 2 | 0.2108 | hour-ahead |  | 32 | ANN |  | 35 | Persistence Farm 2 | 
 |  | 3 | Surface Pressure |  | 17 |  | Persistence Farm 3 | 0.1393 | hour-ahead |  | 33 | SVR |  | 36 | Persistence Farm 3 | 
 |  | 4 | Relative Humidity |  | 18 |  | MLR | 0.0763 | day-ahead |  |  |  |  | 37 | MLR | 
 |  | 5 | Cloud Cover |  | 19 |  | ANN | 0.0681 | day-ahead |  | No. | Variable Name |  | 38 | ANN | 
 |  | 6 | 10m- U Wind |  | 20 |  | SVR | 0.0715 | day-ahead |  | 50 | std. dev (all ramp rates) |  | 39 | SVR | 
 |  | 7 | 10m- V Wind |  | 21 |  | Combined 0.0628 | 0.0628 | hour-ahead |  |  |  |  | 40 | Combined 0.0628 | 
 |  | 8 | 2-m Temperature |  | 22 |  | Combined 0.0554 | 0.0554 | hour-ahead |  |  |  |  | 41 | Combined 0.0554 | 
 |  | 9 | Surface solar radiation down |  | 23 |  | Combined 0.0523 | 0.0523 | hour-ahead |  |  |  |  | 42 | Combined 0.0523 | 
 |  | 10 | Surface thermal radiation down |  | 24 |  | Combined 0.0579 | 0.0579 | hour-ahead |  |  |  |  | 43 | Combined 0.0579 | 
 |  | 11 | Top net solar radiation |  | 25 |  | ARIMA 0.0928 | 0.0928 | hour-ahead |  |  |  |  | 44 | ARIMA 0.0928 | 
 |  | 12 | Total precipitation |  | 26 |  | ARIMAX 0.0915 | 0.0915 | hour-ahead |  |  |  |  | 45 | ARIMAX 0.0915 | 
 |  | 13 | Heat Index |  | 27 |  | NAR Hr1 | 0.0890 | hour-ahead |  |  |  |  | 46 | NAR Hr1 | 
 |  | 14 | Wind Speed |  | 28 |  | NAR Hr2 | 0.1384 | hour-ahead |  |  |  |  | 47 | NAR Hr2 | 
 |  |  |  |  | 29 |  | NARX Hr1 | 0.0760 | hour-ahead |  |  |  |  | 48 | NARX Hr1 | 
 |  |  |  |  | 30 |  | NARX Hr2 | 0.1419 | hour-ahead |  |  |  |  | 49 | NARX Hr2 | 
 | Solar power forecasts & their ramp rates
51 | Persistence Farm 1
52 | Persistence Farm 2
53 | Persistence Farm 3
54 | MLR
55 | ANN
56 | SVR
57 | Combined 0.0628
58 | Combined 0.0554
59 | Combined 0.0523
60 | Combined 0.0579
61 | ARIMA 0.0928
62 | ARIMAX 0.0915
63 | NAR Hr1
64 | NAR Hr2
65 | NARX Hr1
66 | NARX Hr2
Classes of the Forecasts
Combined Forecasts of Ramps
39
 | Classes (Labels) of Ramp Event
Additional Features:
Modeling and Results

## Slide 40
Class | Class1 | Class2 | Class3 | Total
Samples | 131 | 31 | 3666 | 3828
For clarity, low-rate classes (2&4) become as a one class, class3: 
Data projection onto PC1 and PC2:
Threshold=0.4pu/hr
3) All 50 Features (add ramp rates of forecasts)
4) All 66 Features (add class labels of forecasts)
1) All 14 weather variables
2) All 30 Features (add solar power forecasts)
40
Combined Forecasts of Ramps
Modeling and Results

## Slide 41
Model | Parameters | Selected Features
Naïve Bayes | Distribution=Normal; distribution parameters are estimated in the training. | 1, 5, 11
LDA | Its coefficients (μ) are fitted in the training. | 1, 2, 3, 6, 9, 10, 12
Decision Tree | Max of splits=15; Min leaf size=1 | 1, 12
kNN | Euclidean distance; k=15 (nearest 15 neighbors) | 1, 4, 6, 7, 8
Logistic Regression | Its coefficients (β) are fitted in the training. | 1, 3, 11, 12
Random Forests | Forest size=100 trees; Min. leaf size=1 | 1, 3, 11, 12
SVM | Kernel= Radial basis function; C=184; gamma=5 | 1, 3, 11, 12
ANN | Hidden layer=1; Neurons=10 | 1, 5, 12
(a)
(b)
No. | Most Important Features
1 | Cloud water content, NWP output
2 | Cloud cover, NWP output
3 | Top net solar radiation, NWP output
4 | Hour-ahead combined forecasts of solar power
5 | Ramp rates of NWP-driven day-ahead solar power forecasts by ANN
6 | Ramp rates of NWP-driven day-ahead solar power forecasts by SVR
7 | Ramp rates of hour-ahead combined forecasts of solar power
8 | Ramp rates of time-series hour-ahead forecasts of solar power by NARX
9 | Ramp classes of persistence hour-ahead forecasts of solar power
10 | Ramp classes of NWP-drive day-ahead solar power forecasts by ANN
11 | Ramp classes of NWP-driven day-ahead solar power forecasts by SVR
12 | Ramp classes of hour-ahead combined forecasts of solar power
(a) The most 12 important features out of 66; (b) selected features and parameters for each model
41
Combined Forecasts of Ramps
Modeling and Results

## Slide 42
Solar power ramp event forecasts of the high-rate ramp events, (|Rate| ≥ 0.4 pu/hr = 162 events)
by the classification techniques.
Method | Naïve Bayes | LDA | Decision Trees | kNN | Logistic Regression | Random Forest | SVM | ANN | Combined Classifiers
Precision (%) | 62% | 65% | 73% | 68% | 79% | 79% | 77% | 70% | 79%
Recall (%) | 43% | 40% | 38% | 31% | 30% | 43% | 43% | 38% | 50%
Balanced Precision (%) | 75% | 78% | 80% | 78% | 59% | 80% | 80% | 78% | 87%
F1-Score (%) | 51% | 49% | 50% | 43% | 44% | 56% | 55% | 49% | 61%
Diff. Index | 27 | 30 | 38 | 27 | 36 | 51 | 48 | 35 | 60
Chart: Percentage (%)
| Naïve Bayes | LDC | DT | kNN | Logistic | RF-Classification | SVM | ANN | Combined Classifiers
Precision (%) | 0.62 | 0.65 | 0.72619 | 0.68493 | 0.79 | 0.79 | 0.77 | 0.7 | 0.79
Recall (%) | 0.4321 | 0.39506 | 0.37654 | 0.30864 | 0.30247 | 0.4321 | 0.42593 | 0.37654 | 0.5
Balanced Precision (%) | 0.75 | 0.78 | 0.79562 | 0.78074 | 0.59 | 0.8 | 0.8 | 0.78 | 0.87
F1-Score | 0.50927 | 0.49144 | 0.49593 | 0.42553 | 0.43745 | 0.55864 | 0.54847 | 0.48968 | 0.61358
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Diff(True-False) | 27 | 30 | 38 | 27 | 36 | 51 | 48 | 35 | 60
42
Combined Forecasts of Ramps
Modeling and Results

## Slide 43
Block diagram of the adjusting approach of solar power ramp event forecasting
Combined Forecasts of Ramps
Distribution of the classes of solar power ramp events at threshold (Tsh) =0.4pu/hr.
Implementing the adjusting approach
to forecasts solar power ramp events
Modeling and Results
Solar Ramp Events
Ramp-Down Events
Ramp-Up Events
Low-Rate
High-Rate
Low-Rate
High-Rate
Class1
Rate ≥ +Tsh
Class2
0 ≤ Rate < +Tsh
Class3
Rate ≤ −Tsh
Class4
0 ≥ Rate > −Tsh

## Slide 44
Chart: Evaluation of Solar Power Ramp Event Forecasts by Using Different Evaluation Metrics
| Persistence, PV1 | NARX | Simple Average (NARX, MLR, ANN, SVR) | Combined Forecasts | Adjust Approach (Pers.1) | RF-Regression | Adjust Approach (Pers.1,3 +NARX +Clouds) | Probabilistc Forecasts (Q1 to Q99) | Probabilistc Forecasts (Q25 to Q75)
Precision (%) | 0.0045 | 0.45 | 0.67 | 0.74 | 0.75 | 0.81 | 0.87 | 0.88 | 0.81
Recall (%) | 0.0045 | 0.055556 | 0.32099 | 0.28395 | 0.38889 | 0.49383 | 0.51235 | 0.53086 | 0.66667
Balanced Precision (%) | 0.34 | 0.61 | 0.8 | 0.79 | 0.83 | 0.81 | 0.86 | 0.9 | 0.88
F1-Score (%) | 0.0045 | 0.098901 | 0.43404 | 0.41042 | 0.5122 | 0.6449 | 0.6449 | 0.66223 | 0.73138
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Diff(True-False) | 0.2 | -2 | 26 | 30 | 42 | 61 | 71 | 74 | 83
 | Persistence, PV1 | NARX | Simple Average (NARX, MLR, ANN, SVR) | Combined (Pers.1, MLR, ANN, SVR) | Adjust Approach (Pers.1, MLR, ANN, SVR) | Combined (Pers.1&3 +NARX, Clouds, MLR, ANN, SVR) | Adjust Approach (Pers.1&3 +NARX, Clouds, MLR, ANN, SVR) | Probabilistic Forecasts (Q1 to Q99) | Probabilistic Forecasts (Q25 to Q75)
Precision (%) | 0% | 45% | 67% | 74% | 75% | 81% | 87% | 88% | 81%
Recall (%) | 0% | 6% | 32% | 28% | 39% | 49% | 51% | 53% | 67%
Balanced Precision (%) | 34% | 61% | 80% | 79% | 83% | 81% | 86% | 90% | 88%
F1-Score (%) | 0% | 10% | 43% | 41% | 51% | 64% | 64% | 66% | 73%
Diff(True-False) | 0 | -2 | 26 | 30 | 42 | 61 | 71 | 74 | 83
Combined Forecasts of Ramps
Solar power ramp event forecasts of the high-rate ramp events, (|Rate| ≥ 0.4 pu/hr = 162 events) by the adjusting approach
Modeling and Results
Implementing the adjusting approach to forecasts solar power ramp events

## Slide 45
Chart: Certainty of HR (%)
| [0-0.1) | [0.1-0.2) | [0.2-0.3) | [0.3-0.4) | [0.4-0.5) | [0.5-0.6) | [0.6-0.7) | [0.7-0.8)
Average of Certainty | 0.0042082 | 0.004421 | 0.019728 | 0.14757 | 0.42787 | 0.6778 | 0.88091 | 0.935
Std. Dv. of Certainty | 0.028663 | 0.028858 | 0.055435 | 0.15721 | 0.26414 | 0.27701 | 0.17172 | 0.091924
The certainty forecasts for high-rate (HR) events by the adjusting approach for different ranges of ramp rates when threshold=0.4 pu/hr
Chart: Certainty of HR (%)
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7
Average of Certainty | 0.78066 | 0.64087 | 0.58587 | 0.52815 | 0.43593 | 0.36385 | 0.12
Std. Dv. of Certainty | 0.25307 | 0.31286 | 0.32681 | 0.30054 | 0.28513 | 0.24754 | 0.014142
Threshold ¦pu/hr¦ | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7
Ramp Events | 2041 | 858 | 380 | 162 | 54 | 13 | 2
 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7
Ramp Events | 2041 | 858 | 380 | 162 | 54 | 13 | 2
The certainty of forecasts for high-rate (HR) events by the adjusting approach with different thresholds,
Tsh=0.1 to 0.7 pu/hr
Combined Forecasts of Ramps
The uncertainty analysis
Modeling and Results
,
Range of Rates, ¦p.u/hr¦ | [0-0.1) | [0.1-0.2) | [0.2-0.3) | [0.3-0.4) | [0.4-0.5) | [0.5-0.6) | [0.6-0.7) | [0.7-0.8)
Ramp Events | 1787 | 1183 | 478 | 218 | 108 | 41 | 11 | 2

## Slide 46
Golden – August 14, 2012, through September 24, 2013, semi-arid climate.
Cocoa – January 21, 2011, through March 4, 2012, subtropical climate.
Eugene – December 20, 2012, through January 20, 2014, marine west coast climate.
Weather variables (measurements) | 
Plane-of-Array (POA) Irradiance (W/m2) | Amount of solar irradiance received on the PV panel surface
Back-Surface Temperature of PV Panel (◦C) | PV panel back-surface temperature, measured behind the center of PV panel
Relative Humidity (%) | Relative humidity at the site
Precipitation (mm) | Accumulated daily total precipitation in millimeter
Direct Normal Irradiance (DNI) (W/m2) | Amount of solar irradiance received within a 5.7◦ field-of-view centered on the sun
Global Horizontal Irradiance (GHI) (W/m2) | Total amount of direct and diffuse solar irradiance received on a horizontal surface
Diffuse Horizontal Irradiance (DHI) (W/m2) | Amount of solar irradiance received from the sky (excluding the solar disk) on a horizontal surface
* L. J. Tashman, Out-of-sample tests of forecasting accuracy: an analysis and review," International journal of forecasting, vol. 16, no. 4, pp. 437-450, 2000.
Data partition into training and testing sets:
The cross-validation strategy is adopted
Available data
In this study the adjusting approach is implemented for intra-hour forecasts.
This study also serves as an out-of-sample test* to verify the adjusting approach performance.
3 Forecast horizons (15, 30, 60min) for 3 sites, (Golden, CO, Cocoa, FL, Eugene, OR) 9 cases.
Data Description:
Intra-Hour Forecasts
Modeling and Results

## Slide 47
Location | Horizon | Persistence |  |  | NAR |  |  | ARIMA |  |  | ANN |  |  | ELM |  | 
 |  | RMSE | MAE | MBE | RMSE | MAE | MBE | RMSE | MAE | BIAS | RMSE | MAE | MBE | RMSE | MAE | MBE
Golden | 15min | 0.0344 | 0.0255 | 0.2394 | 0.0327 | 0.0235 | -4.647 | 0.0346 | 0.0254 | -0.0007 | 0.0344 | 0.0257 | -5.276 | 0.0340 | 0.0254 | -0.969
 | 30min | 0.0481 | 0.0365 | 0.2113 | 0.0434 | 0.0322 | -2.108 | 0.0459 | 0.0346 | -0.3162 | 0.0432 | 0.0322 | -7.525 | 0.0464 | 0.0345 | -2.022
 | 60min | 0.0715 | 0.0541 | 0.2113 | 0.0586 | 0.0438 | -6.070 | 0.0608 | 0.0462 | 0.8859 | 0.0571 | 0.0431 | -3.672 | 0.0646 | 0.0465 | 3.773
Cocoa | 15min | 0.0411 | 0.0303 | 0.3746 | 0.0390 | 0.0269 | -6.028 | 0.0405 | 0.0287 | 0.3298 | 0.0384 | 0.0274 | -9.703 | 0.0408 | 0.0302 | -0.904
 | 30min | 0.0553 | 0.0417 | 0.3005 | 0.0479 | 0.0315 | -2.244 | 0.0470 | 0.0334 | 0.2949 | 0.0451 | 0.0307 | 2.389 | 0.0492 | 0.0325 | -0.482
 | 60min | 0.0870 | 0.0678 | 0.4302 | 0.0587 | 0.0420 | -7.261 | 0.0595 | 0.0427 | -0.1683 | 0.0562 | 0.0394 | -2.768 | 0.0579 | 0.0413 | 0.107
Eugene | 15min | 0.0358 | 0.0235 | 0.2126 | 0.0360 | 0.0238 | 0.939 | 0.0355 | 0.0219 | 0.2201 | 0.0350 | 0.0215 | -5.825 | 0.0344 | 0.0215 | -2.752
 | 30min | 0.0483 | 0.0344 | 0.2144 | 0.0425 | 0.0271 | -7.997 | 0.0442 | 0.0281 | -2.9847 | 0.0425 | 0.0270 | 3.761 | 0.0421 | 0.0270 | -3.048
 | 60min | 0.0738 | 0.0561 | 0.2144 | 0.0586 | 0.0397 | 0.187 | 0.0616 | 0.0415 | -0.0845 | 0.0575 | 0.0397 | -3.480 | 0.0568 | 0.0394 | -3.485
Total Average |  | 0.0550 | 0.0411 | 0.2676 | 0.0464 | 0.0323 | -3.9143 | 0.0477 | 0.0336 | -0.2026 | 0.0455 | 0.0319 | -3.5665 | 0.0474 | 0.0332 | -1.0871
Forecast | Persist | NAR | ARIMA | ANN | ELM
RMSEavg | 0.0550 | 0.0464 | 0.0477 | 0.0455 | 0.0474
MAEavg | 0.0411 | 0.0323 | 0.0336 | 0.0319 | 0.0332
BIASavg | 0.2676 | -3.9143 | -0.2026 | -3.5665 | -1.0871
Intra-Hour Forecasts
The aggregated* evaluation of the individual intra-hourly forecasts of solar power
The individual intra-hourly forecasts of solar power
*Aggregation is conducted by taking the average of the evaluating values of all 3 horizons and 3 sites.
Modeling and Results

## Slide 48
Block diagram of the adjusting approach for intra-hour forecasts of solar power and ramp events
Intra-Hour Forecasts
Implementing the adjusting approach to forecasts solar power ramp events
Modeling and Results

## Slide 49
Intra-Hour Forecasts
Chart: Improvement (%)
| Persistence | NAR | ARIMA | ANN | ELM | Simple Average
 | 0.43711 | 0.33174 | 0.34936 | 0.319 | 0.34307 | 0.15796
Average improvements of the combined forecasts by the adjusting approach with respect to other forecasts
Modeling and Results
Location | Forecast Horizon | RMSE |  |  |  |  |  | 
 |  | Persist. | NAR | ARIMA | ANN | ELM | Simple Average | Adjusting Approach
Golden | 15min | 0.0344 | 0.0327 | 0.0346 | 0.0344 | 0.0340 | 0.0322 | 0.0246
 | 30min | 0.0481 | 0.0434 | 0.0459 | 0.0432 | 0.0464 | 0.0328 | 0.0280
 | 60min | 0.0715 | 0.0586 | 0.0608 | 0.0571 | 0.0637 | 0.0484 | 0.0453
Cocoa | 15min | 0.0411 | 0.0389 | 0.0405 | 0.0384 | 0.0408 | 0.0288 | 0.0240
 | 30min | 0.0553 | 0.0478 | 0.0470 | 0.0451 | 0.0484 | 0.0345 | 0.0288
 | 60min | 0.0870 | 0.0587 | 0.0594 | 0.0562 | 0.0578 | 0.0511 | 0.0420
Eugene | 15min | 0.0358 | 0.0360 | 0.0355 | 0.0350 | 0.0344 | 0.0255 | 0.0193
 | 30min | 0.0483 | 0.0425 | 0.0441 | 0.0425 | 0.0421 | 0.0313 | 0.0257
 | 60min | 0.0738 | 0.0586 | 0.0607 | 0.0575 | 0.0568 | 0.0465 | 0.0411
Average |  | 0.0550 | 0.0464 | 0.0476 | 0.0455 | 0.0472 | 0.0368 | 0.0310

## Slide 50
Location | Forecast Horizon | Pinball (PB) |  |  | 
 |  | Persistence | AnEn Simple Average | AnEn Adjusting Approach | Ensemble Adjusting Approach
Golden | 15min | 0.0236 | 0.0098 | 0.0071 | 0.0064
 | 30min | 0.0271 | 0.0102 | 0.0084 | 0.0077
 | 60min | 0.0289 | 0.0162 | 0.0141 | 0.0124
Cocoa | 15min | 0.0277 | 0.0082 | 0.0069 | 0.0063
 | 30min | 0.0304 | 0.0101 | 0.0081 | 0.0073
 | 60min | 0.0319 | 0.0166 | 0.0123 | 0.0109
Eugene | 15min | 0.0316 | 0.0067 | 0.0053 | 0.0046
 | 30min | 0.0370 | 0.0087 | 0.0072 | 0.0062
 | 60min | 0.0415 | 0.0148 | 0.0126 | 0.0106
Average |  | 0.0311 | 0.0113 | 0.0091 | 0.0080
Intra-Hour Forecasts
Probabilistic Forecasts
Modeling and Results
Pbq,i (Fq, ) =
Quantiles, q[1- 99]

## Slide 51
Chart: Evaluation of Solar Power Ramp Event Forecasts by Using Different Evaluation Metrics
| NAR | ARIMA | ANN | ELM | Simple Avg. | Adj Apraoach
Precision (%) | 0.39 | 0.36 | 0.45 | 0.33 | 0.69 | 0.6
Recall (%) | 0.13 | 0.09 | 0.14 | 0.11 | 0.24 | 0.48
Balanced Precision (%) | 0.5 | 0.46 | 0.53 | 0.47 | 0.71 | 0.69
F1 Score (%) | 0.19 | 0.12 | 0.2 | 0.15 | 0.29 | 0.53
Pad | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0
Diff. Index | 19 | 17 | 31 | 18 | 34 | 79
Forecasts | NAR | ARIMA | ANN | ELM | Simple Avg. | Adj. Approach
Precision (%) | 39% | 36% | 45% | 33% | 69% | 60%
Recall (%) | 13% | 9% | 14% | 11% | 24% | 48%
Balanced Precision (%) | 50% | 46% | 53% | 47% | 71% | 69%
F1 Score (%) | 19% | 12% | 20% | 15% | 29% | 53%
Diff. Index | 19 | 17 | 31 | 18 | 34 | 79
Intra-hour forecasts of solar power ramp events of the high-rate ramp events,
(|Rate| ≥ 0.1 pu/dt) by the adjusting approach.
Intra-Hour Forecasts
Modeling and Results

## Slide 52
Location | Australia | Golden, CO | Cocoa, FL | Eugene, OR
RMSE | 0.0523 | 0.0453 | 0.0420 | 0.0411
Pinball | 0.0084 | 0.0124 | 0.0109 | 0.0106
Comparison the hourly forecasts of solar power by the adjusting approach with different datasets
Comparison of Hourly Forecasts
Dataset | Golden, CO | Cocoa, FL | Eugene, OR | Canberra
Country | USA | USA | USA | Australia
Climate type | Semi-arid | Subtropical | Marine coast | Oceanic
Latitude (°, -S) | 39.74 | 28.39 | 44.05 | -35.16
Longitude (°, -W) | -105.18 | -80.46 | -123.07 | 149.06
Elevation above sea (m) | 1798 | 12 | 145 | 595
Number of panels | 11 | 11 | 11 | 8
Panel tilt (°) from horizontal | 40 | 28.5 | 44 | 36
Panel orientation (°) clockwise from North | 180 | 180 | 180 | 38
Total capacity (W) | 1252 | 1272 | 1290 | 1560
Time period of observations | Aug. 2012 to Sep. 2013 | Jan. 2011 to March 2012 | Dec. 2012 to Jan. 2014 | April 2012 to May 2014
Data resolution | 15min | 5min | 5min | 1hr
Missing (% of observations) | 18% | 17% | 10% | 0%
Variability (data resolution) Std.Div. | (15min) 0.256 (1hr) 0.119 | (5min) 0.251 (1hr) 0.164 | (5min) 0.250 (1hr) 0.161 | (1hr) 0.259
Specifications of solar PV systems and data statistics
Modeling and Results

## Slide 53
Conclusions
The adjusting approach improves the combined forecasts.
The approach is simple vs. the classification techniques.
Ramp classes more separable with features: forecasts, ramp-rates, clouds, neighboring PVs.
Most effective weather variables:
Cloud information: cloud type, height and cloud formation.
Clear-sky solar irradiance / Top solar irradiance at Earth's atmospheric layer.
Diff. Index of high-rate ramps is efficient for the imbalanced classification.
Probabilistic forecasts as a tool of situational awareness.

## Slide 54
A direct comparison between the satellite-driven forecasts and the proposed approach.
Datasets with more different levels of variability of solar power.
Applying the adjusting approach to forecast wind power ramp events.
Assimilating power of neighboring PV systems, sky imaging and satellite data.
Using operational weather forecasts of high-resolution rabid refresh (HRRR) model.
Future Work
Recommendations and further work for this dissertation are as follows:

## Slide 55
M. Abuella and B. Chowdhury, “Solar Power Probabilistic Forecasting by Using Multiple Linear Regression Analysis,” in IEEE Southeast Con. Proceedings, 2015.
M. Abuella and B. Chowdhury, “Solar Power Forecasting using Artificial Neural Networks,” in North American Power Symposium (NAPS), 2015.
M. Abuella and B. Chowdhury, “Solar Power Forecasting Using Support Vector Regression,” in Proceedings of the American Society for Engineering Management 2016 International Annual Conference, 2016.
M. Abuella and B. Chowdhury, “Random forest ensemble of support vector regression models for solar power forecasting,” in 2017 IEEE Power Energy Society Innovative Smart Grid Technologies Conference (ISGT), 2017.
M. Abuella and B. Chowdhury, “Hourly probabilistic forecasting of solar power,” in 2017 North American Power Symposium (NAPS), 2017.
M. Abuella and B. Chowdhury, “Forecasting Solar Power Ramp Events Using Machine Learning Classification Techniques,” in 2018 IEEE 8th International Symposium on Power Electronics for Distributed Generation Systems (PEDG), 2018.
M. Abuella and B. Chowdhury, “Qualifying Combined Solar Power Forecasts in Ramp Events’ Perspective,” in IEEE Power & Energy Society General Meeting, 2018.
M. Abuella, & B. Chowdhury, “Improving Combined Solar Power Forecasts Using Estimated Ramp Rates: Data-driven Post-processing Approach,” IET Renewable Power Generation Journal, 2018.
M. Abuella, & B. Chowdhury, “Forecasting of Solar Power Ramp Events: A post Processing Approach,” Renewable Energy, 2018.
Vita
Dissertation-based Publications
https://www.researchgate.net/publication/328757565_A_Post-processing_Approach_for_Solar_Power_Combined_Forecasts_of_Ramp_Events/download

## Slide 56
Thanks for Your Listening
Any Question?
https://epic.uncc.edu
Energy Production and Infrastructure Center
University of North Carolina at Charlotte
Mohamed Ali Abuella
mabuella@uncc.edu
A Post-processing Approach for Solar Power Combined Forecasts of Ramp Events