## Slide 1
A Post-processing Approach for Solar Power Combined Forecasts of Ramp Events
Mohamed Abuella
Supervised by:
Prof. Badrul Chowdhury
A dissertation submitted to the faculty of
The University of North Carolina at Charlotte
in partial fulfillment of the requirements
for the degree of Doctor of Philosophy in
Electrical Engineering
Charlotte
October 1st, 2018

## Slide 2
A post-processing approach combines and improves solar power forecasts.
The approach also adjusts the combined forecasts in terms of ramp events.
A classification of all possible thresholds and classes of ramp event forecasts.
A customized cost function for imbalanced classification of ramp events.
Suitable metrics for the feature selection process and performance evaluation.
An uncertainty analysis for probabilistic forecasts of solar power ramp events.
Highlights

## Slide 3
Illustration of the motivation of PV solar power forecasts
PV Solar Power Generations
are Too Variable
Reducing
Cost
and Pollution
PSupply = PDemand +PLoss
Coordination with Operating Reserves and Energy Storage
Systems
Why Forecast?
Motivation

## Slide 4
# M. Sengupta, A. Habte, C. Gueymard, S. Wilbert, and D. Renne, Best practices handbook for the collection and use of solar resource data for solar energy applications," Tech. rep., National Renewable Energy Lab.(NREL), Golden, CO (United States), 2017
Literature Review
Yang, D., Kleissl, J., Gueymard, C. A., Pedro, H. T., & Coimbra, C. F. (2018). History and trends in solar irradiance and PV power forecasting: A preliminary assessment and review using text mining. Solar Energy. (**This review paper published in 2018, and reviewing 1000 solar forecast studies).
Taxonomy of solar forecasting methods based on temporal and spatial resolution#
CM-sat: cloud motion by satellite images;
CM-SI: cloud motion by sky-imagers
NWP: Numerical weather prediction Systems
Statistical models: blending and post-processing all of the methodologies.

## Slide 5
Problem Statement and Contribution
Kleissl, J. (2013). Solar energy forecasting and resource assessment. Academic Press.
Inman, R. H., Pedro, H. T., & Coimbra, C. F. (2013). Solar forecasting methods for renewable energy integration. Progress in energy and combustion science, 39(6), 535-576.
Combining of different forecasts can reduce the systemic bias of the individual models, boost the overall accuracy, and make the performance more robust, but it also smooths out the sharp changes of the forecasts, which leads to reduced accuracy of the combined forecasts for ramp events.
The Problem Statement
The post-processing methods (MOS) are affecting the ramp event forecasts by smoothing the sharp changes in the raw forecasts. (Kleissl 2013; Inman et al. 2013)

## Slide 6
Problem Statement and Contribution
Due to the issue that was highlighted (Kleissl 2013; Inman et al. 2013), it is therefore, there is room for improvement by applying the proposed approach for adjusting the combined forecasts of solar power in terms of ramp events.
To the best of our knowledge, this is the first attempt to tackle this issue of the combined forecasts for solar power ramp events.
The Contribution
A post-processing approach combines and improves solar power forecasts.
The approach also adjusts the combined forecasts in terms of ramp events.
A classification of all possible thresholds and classes of ramp event forecasts.
A customized cost function for imbalanced classification of ramp events.
Suitable metrics for the feature selection process and performance evaluation.
An uncertainty analysis for probabilistic forecasts of solar power ramp events.

## Slide 7
Flowchart of Solar Power Forecasts
Graphical Abstract of the Proposed Adjusting Approach

## Slide 8
Block diagram of the adjusting approach
Random
Forest
fit by
MSE
F
&
MSE
RR
Day
-
ahead Forecasts
including the past forecasts
Outcomes
:
MLR
,
ANN
,
SVR
Hour
-
ahead Forecasts
including the past forecasts
Outcomes
:
Persistence and
Combined Forecasts
Ramp Rates of
Day
-
ahead
Forecasts
Adjusted Hour
-
ahead Forecasts
Ramp Rates of
Hour
-
ahead
Forecasts
Combining by
Random Forest
Statistical
&
AI Models
Weather Data
(
NWP
)
PV System
Data
Persistence
Model
Forecasting Stage
Combining Stage
Adjusting Stage
Graphical Abstract of the Proposed Adjusting Approach

## Slide 9
Block diagram of the adjusting approach
Flowchart of Solar Power Forecasts
Pre
-
Processing
·
Outlier detection and
data cleansing
·
Feature engineering
Weather Data
·
Solar irradiance
·
Temperature
·
Cloud coverage
·
Humidity
·
...
etc
.
PV System Data
·
Measured PV power output
·
Location and modules type
,
orientation
,
tilt
,
..
etc
.
Forecasting Models
·
Persistence model
·
Statistical models
·
Artificial intelligence models
Point forecast
Post
-
Processing
·
Ensemble
·
Analog ensemble
Probabilistic forecast
Combining the models’ outcomes
by ensemble learning
Random
Forest
fit by
MSE
F
&
MSE
RR
Day
-
ahead Forecasts
including the past forecasts
Outcomes
:
MLR
,
ANN
,
SVR
Hour
-
ahead Forecasts
including the past forecasts
Outcomes
:
Persistence and
Combined Forecasts
Ramp Rates of
Day
-
ahead
Forecasts
Adjusted Hour
-
ahead Forecasts
Ramp Rates of
Hour
-
ahead
Forecasts
Combining by
Random Forest
Statistical
&
AI Models
Weather Data
(
NWP
)
PV System
Data
Persistence
Model
Forecasting Stage
Combining Stage
Adjusting Stage
Graphical Abstract of the Proposed Adjusting Approach

## Slide 10
Ramp Events During a Cloudy Day
Some ramps are with low rates, while others with high rates.
Ramp rate, =
Ramp rate, =
For the illustrated cloudy day below:
where P(t) is the solar power of the target hour, it can also be its forecast F(t); D is the time duration for which the ramp rate is determined.
Solar Power Ramp Rates
Solar power ramp rate (RR) is the change of solar power during a certain time interval.

## Slide 11
There are several applications of power systems that rely on solar power ramp event forecasts
Potential Applications
Optimizing the voltage regulation equipment.
Control schemes of energy storage systems.
EPEX: European power exchange spot trading
Optimizing the Transformer's Tap Changer position sequences using the solar forecast
Trading & dispatching the operating reserve.
Managing the ramp capability / system flexibility with high-level of renewable energy integration.
Distribution level:
Transmission / bulk level:

## Slide 12
Data Preprocessing
Data Description:
B. Marion, A. Anderberg, C. Deline, J. del Cueto, M. Muller, G. Perrin, J. Rodriguez, S. Rummel, T. J. Silverman, F. Vignola, et al., New data set forvalidating pv module performance models," in Photovoltaic Specialist Conference (PVSC), 2014 IEEE 40th, pp. 1362{1366, IEEE, 2014.
https://crowdanalytix.com/contests/global-energy-forecasting-competition-2014-probabilistic-solar-power-forecasting
Dataset | Golden, CO | Cocoa, FL | Eugene, OR | Canberra
Country | USA | USA | USA | Australia
Climate type | Semi-arid | Subtropical | Marine coast | Oceanic
Latitude (°, -S) | 39.74 | 28.39 | 44.05 | -35.16
Longitude (°, -W) | -105.18 | -80.46 | -123.07 | 149.06
Elevation above sea (m) | 1798 | 12 | 145 | 595
Number of panels | 11 | 11 | 11 | 8
Panel tilt (°) from horizontal | 40 | 28.5 | 44 | 36
Panel orientation (°) clockwise from North | 180 | 180 | 180 | 38
Total capacity (W) | 1252 | 1272 | 1290 | 1560
Time period of observations | Aug. 2012 to Sep. 2013 | Jan. 2011 to March 2012 | Dec. 2012 to Jan. 2014 | April 2012 to May 2014
Data resolution | 15min | 5min | 5min | 1hr
Missing (% of observations) | 18% | 17% | 10% | 0%
Variability (data resolution) Std.Div. | (15min) 0.256 (1hr) 0.119 | (5min) 0.251 (1hr) 0.164 | (5min) 0.250 (1hr) 0.161 | (1hr) 0.259

## Slide 13
Model N
Weather Data
Ensemble Learning (RF) for Combining of Forecasts
Combined Forecasts
Individual Forecasts of PV Solar Power Ramp Events
Model A
Model B
Fcomb=WA*MA+ WB*MB + WC*MC ….+ WN*MN
Methodology
Method of Combining The Models
Random forest (RF) is chosen to be the ensemble learning method for combining the various models’ outcomes.
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.
Ensemble Forecasts: Combining Various Models
General diagram of combining different models

## Slide 14
Ramp Classes as following:
Class1: Ramp up of high rate, Tsh
Class2: Ramp up of low rate, |rate| Tsh
Class3: Ramp down of high rate, |rate|Tsh
Class4: Ramp down of low rate, |rate| Tsh
Combined Forecasts of Ramps
Modeling and Results
Objective: Increase the true events, Decrease the false events.
& F
Implementing several classification models to forecasts solar power ramp events
Distribution of the classes of solar power ramp events at threshold (Tsh) =0.4pu/hr.
Classes of solar power ramp events in the case study

## Slide 15
Class | Class1 | Class2 | Class3 | Total
Samples | 131 | 31 | 3666 | 3828
For clarity, low-rate classes (2&4) become as a one class, class3: 
Data projection onto PC1 and PC2:
Threshold=0.4pu/hr
3) All 50 Features (add ramp rates of forecasts)
4) All 66 Features (add class labels of forecasts)
1) All 14 weather variables
2) All 30 Features (add solar power forecasts)
15
Combined Forecasts of Ramps
Modeling and Results

## Slide 16
Solar power ramp event forecasts of the high-rate ramp events, (|Rate| ≥ 0.4 pu/hr = 162 events)
by the classification techniques.
Method | Naïve Bayes | LDA | Decision Trees | kNN | Logistic Regression | Random Forest | SVM | ANN | Combined Classifiers
Precision (%) | 62% | 65% | 73% | 68% | 79% | 79% | 77% | 70% | 79%
Recall (%) | 43% | 40% | 38% | 31% | 30% | 43% | 43% | 38% | 50%
Balanced Precision (%) | 75% | 78% | 80% | 78% | 59% | 80% | 80% | 78% | 87%
F1-Score (%) | 51% | 49% | 50% | 43% | 44% | 56% | 55% | 49% | 61%
Diff. Index | 27 | 30 | 38 | 27 | 36 | 51 | 48 | 35 | 60
Chart: Percentage (%)
| Naïve Bayes | LDC | DT | kNN | Logistic | RF-Classification | SVM | ANN | Combined Classifiers
Precision (%) | 0.62 | 0.65 | 0.72619 | 0.68493 | 0.79 | 0.79 | 0.77 | 0.7 | 0.79
Recall (%) | 0.4321 | 0.39506 | 0.37654 | 0.30864 | 0.30247 | 0.4321 | 0.42593 | 0.37654 | 0.5
Balanced Precision (%) | 0.75 | 0.78 | 0.79562 | 0.78074 | 0.59 | 0.8 | 0.8 | 0.78 | 0.87
F1-Score | 0.50927 | 0.49144 | 0.49593 | 0.42553 | 0.43745 | 0.55864 | 0.54847 | 0.48968 | 0.61358
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Diff(True-False) | 27 | 30 | 38 | 27 | 36 | 51 | 48 | 35 | 60
16
Combined Forecasts of Ramps
Modeling and Results

## Slide 17
Chart: Evaluation of Solar Power Ramp Event Forecasts by Using Different Evaluation Metrics
| Persistence, PV1 | NARX | Simple Average (NARX, MLR, ANN, SVR) | Combined Forecasts | Adjust Approach (Pers.1) | RF-Regression | Adjust Approach (Pers.1,3 +NARX +Clouds) | Probabilistc Forecasts (Q1 to Q99) | Probabilistc Forecasts (Q25 to Q75)
Precision (%) | 0.0045 | 0.45 | 0.67 | 0.74 | 0.75 | 0.81 | 0.87 | 0.88 | 0.81
Recall (%) | 0.0045 | 0.055556 | 0.32099 | 0.28395 | 0.38889 | 0.49383 | 0.51235 | 0.53086 | 0.66667
Balanced Precision (%) | 0.34 | 0.61 | 0.8 | 0.79 | 0.83 | 0.81 | 0.86 | 0.9 | 0.88
F1-Score (%) | 0.0045 | 0.098901 | 0.43404 | 0.41042 | 0.5122 | 0.6449 | 0.6449 | 0.66223 | 0.73138
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pad | 0 | 0 | 0 | 0 | 0 | 0 | 0
Diff(True-False) | 0.2 | -2 | 26 | 30 | 42 | 61 | 71 | 74 | 83
 | Persistence, PV1 | NARX | Simple Average (NARX, MLR, ANN, SVR) | Combined (Pers.1, MLR, ANN, SVR) | Adjust Approach (Pers.1, MLR, ANN, SVR) | Combined (Pers.1&3 +NARX, Clouds, MLR, ANN, SVR) | Adjust Approach (Pers.1&3 +NARX, Clouds, MLR, ANN, SVR) | Probabilistic Forecasts (Q1 to Q99) | Probabilistic Forecasts (Q25 to Q75)
Precision (%) | 0% | 45% | 67% | 74% | 75% | 81% | 87% | 88% | 81%
Recall (%) | 0% | 6% | 32% | 28% | 39% | 49% | 51% | 53% | 67%
Balanced Precision (%) | 34% | 61% | 80% | 79% | 83% | 81% | 86% | 90% | 88%
F1-Score (%) | 0% | 10% | 43% | 41% | 51% | 64% | 64% | 66% | 73%
Diff(True-False) | 0 | -2 | 26 | 30 | 42 | 61 | 71 | 74 | 83
Combined Forecasts of Ramps
Solar power ramp event forecasts of the high-rate ramp events, (|Rate| ≥ 0.4 pu/hr = 162 events) by the adjusting approach
Modeling and Results
Implementing the adjusting approach to forecasts solar power ramp events

## Slide 18
Location | Australia | Golden, CO | Cocoa, FL | Eugene, OR
RMSE | 0.0523 | 0.0453 | 0.0420 | 0.0411
Pinball | 0.0084 | 0.0124 | 0.0109 | 0.0106
Comparison the hourly forecasts of solar power by the adjusting approach with different datasets
Comparison of Hourly Forecasts
Dataset | Golden, CO | Cocoa, FL | Eugene, OR | Canberra
Country | USA | USA | USA | Australia
Climate type | Semi-arid | Subtropical | Marine coast | Oceanic
Latitude (°, -S) | 39.74 | 28.39 | 44.05 | -35.16
Longitude (°, -W) | -105.18 | -80.46 | -123.07 | 149.06
Elevation above sea (m) | 1798 | 12 | 145 | 595
Number of panels | 11 | 11 | 11 | 8
Panel tilt (°) from horizontal | 40 | 28.5 | 44 | 36
Panel orientation (°) clockwise from North | 180 | 180 | 180 | 38
Total capacity (W) | 1252 | 1272 | 1290 | 1560
Time period of observations | Aug. 2012 to Sep. 2013 | Jan. 2011 to March 2012 | Dec. 2012 to Jan. 2014 | April 2012 to May 2014
Data resolution | 15min | 5min | 5min | 1hr
Missing (% of observations) | 18% | 17% | 10% | 0%
Variability (data resolution) Std.Div. | (15min) 0.256 (1hr) 0.119 | (5min) 0.251 (1hr) 0.164 | (5min) 0.250 (1hr) 0.161 | (1hr) 0.259
Specifications of solar PV systems and data statistics
Modeling and Results

## Slide 19
Conclusions
The adjusting approach improves the combined forecasts.
The approach is simple vs. the classification techniques.
Ramp classes more separable with features: forecasts, ramp-rates, clouds, neighboring PVs.
Most effective weather variables:
Cloud information: cloud type, height and cloud formation.
Clear-sky solar irradiance / Top solar irradiance at Earth's atmospheric layer.
Diff. Index of high-rate ramps is efficient for the imbalanced classification.
Probabilistic forecasts as a tool of situational awareness.

## Slide 20
Thanks for Your Listening
Any Question?
https://epic.uncc.edu
Energy Production and Infrastructure Center
University of North Carolina at Charlotte
Mohamed Ali Abuella
mabuella@uncc.edu
A Post-processing Approach for Solar Power Combined Forecasts of Ramp Events